## Slide 1: Computer Organization and Systems - 03
CPU Performance and RISC Vs CISC

## Slide 2: Topics
CPU Performance
RISC Vs CISC

## Slide 3
WELCOME TO THE POST-PC ERA

## Slide 4: Challenges
Performance Requirement
Energy Efficient

## Slide 5: The 5 Classic Components of a Computer
Input
Output
Memory
Datapath
Control

## Slide 6
DataPath
Control
Processor

## Slide 7: Performance Measurement

## Slide 8
Performance assessment is quite challenging
The scale and intricacy of modern software systems
Wide range of performance improvement techniques employed by hardware designers

## Slide 9
Two perspectives
Mobile Devices
Response time/Execution time
Datacenter Managers/Servers
Throughput/Bandwidth

## Slide 10
Response Time/Execution Time: The total time required for the computer to complete a task, including disk accesses, memory accesses, I/O activities, operating system overhead, CPU execution time etc.
Throughput/Bandwidth: The number tasks completed per unit time
Our focus is Response Time/Execution Time

## Slide 11: Check yourself!
Do the following changes to a computer system increase throughput, decrease response time, or both?
Replacing the processor in a computer with a faster version
Adding additional processors to a system that uses multiple processors for separate tasks- for example, searching the web

## Slide 12: ISA
Instruction: A command that computer hardware understands and obeys.
Instruction Set Architecture (ISA)/Architecture: Programmer’s view of a processor, registers, addressing modes etc.
ISA or instruction set architecture serves as an interface between the hardware and software
ISA can be considered as the specification of a design
By following ISA we can synthesize different processors

## Slide 13: Performance
High performance if the computer executes program faster
CPU time = User CPU time + System CPU time (OS calls)
Elapsed time = User CPU time(time spend executing the lines of code that are in our program)+ System CPU time + wait time ( waiting for I/O + waiting for other running programs)
Our focus is on User CPU time
CPU time = User CPU time

## Slide 14
For a computer X, Performancex = 1/Execution timex
CPU execution time for a program = CPU clock cycles for a program Clock cycle time
CPU execution time for a program = CPU clock cycles for a program /Clock Rate
CPU Clock cycles = Instructions for a program Average Clock cycles per instruction

## Slide 15: CPI
Clock cycles per instruction (CPI) = Average number of clock cycles per instruction for a program or program fragment
Since different instructions may take different amounts of time depending on what they do, CPI is an average of all the instructions executed in the program.
CPI provides one way of comparing two different implementations of the identical instruction set architecture, since the number of instructions executed for a program will, of course, be the same.

## Slide 16: The Classic CPU Performance Equation
CPU time = Instruction count CPI Clock cycle time
CPU time = (Instruction count CPI ) / Clock Rate

## Slide 17: The Classic CPU Performance Equation
Processor Performance = Time / Program
Processor Performance =
Instructions/Program
Code Size
Cycles/Instructions
CPI
Time/Cycle
Cycle Time
Instruction Set Architecture
Implementation
Realization
Compiler Designer
Processor Designer
Chip Designer

## Slide 18
The implementation of the same architecture can be different

## Slide 19: RISC-based Processor

## Slide 20: RISC vs. CISC
CISC(Complex Instruction Set Computer): is a processor design, where single instructions can execute several low-level operations (such as a load from memory, an arithmetic operation, and a memory store) or are capable of multi-step operations or addressing modes within single instructions.
RISC(Reduced Instruction Set Computer): is one whose instruction set architecture (ISA) has a set of attributes that allows it to have a lower cycles per instruction (CPI) than a complex instruction set computer (CISC). Various suggestions have been made regarding a precise definition of RISC, but the general concept is that of a computer that has a small set of simple and general instructions, rather than a large set of complex and specialized instructions. Another common RISC trait is their load/store architecture, where memory is only accessed through specific instructions, rather than as a part of most instructions.
The one typical differentiating characteristic is that most RISC designs use uniform instruction length for almost all instructions, and employ strictly separate load/store-instructions.

## Slide 21
CISC Approach:
the entire task of multiplying two numbers can be completed with one instruction:
MULT 2:3, 5:2
RISC Approach:
LOAD A, 2:3
LOAD B, 5:2
PROD A, B
STORE 2:3, A

## Slide 22: Advantage of RISC
Because each instruction requires only one clock cycle to execute, the entire program will execute in approximately the same amount of time as the multi-cycle "MULT" command. These RISC "reduced instructions" require less transistors of hardware space than the complex instructions, leaving more room for general purpose registers. Because all of the instructions execute in a uniform amount of time (i.e. one clock), pipelining is possible.
Separating the "LOAD" and "STORE" instructions actually reduces the amount of work that the computer must perform. After a CISC-style "MULT" command is executed, the processor automatically erases the registers. If one of the operands needs to be used for another computation, the processor must re-load the data from the memory bank into a register. In RISC, the operand will remain in the register until another value is loaded in its place.

## Slide 23: The Classic CPU Performance Equation
Processor Performance = Time / Program
Processor Performance =
Instructions/Program
Code Size
Cycles/Instructions
CPI
Time/Cycle
Cycle Time
The CISC approach attempts to minimize the number of instructions per program, sacrificing the number of cycles per instruction. RISC does the opposite, reducing the cycles per instruction at the cost of the number of instructions per program.

## Slide 24: RISC-based Processor
By the beginning of the 21st century, the majority of low end and mobile systems relied on RISC architectures. Examples include:
The ARM architecture dominates the market for low power and low cost embedded systems (typically 200–1800 MHz in 2014). It is used in a number of systems such as most Android-based systems, the Apple iPhone and iPad, Microsoft Windows Phone (former Windows Mobile), RIM devices, Nintendo Game Boy Advance, DS / 3DS and Switch etc.
The MIPS line, (at one point used in many SGI computers) and now in the PlayStation, PlayStation 2, Nintendo 64, PlayStation Portable game consoles, and residential gateways like Linksys WRT54G series.
Hitachi's SuperH, originally in wide use in the Sega Super 32X, Saturn and Dreamcast, now developed and sold by Renesas as the SH4
Atmel AVR used in a variety of products ranging from Xbox handheld controllers to BMW cars.
RISC-V, the open source fifth Berkeley RISC ISA, with 32 bit address space, a small core integer instruction set, an experimental "Compressed" ISA for code density and designed for standard and special purpose extensions.

## Slide 25: RISC-based Processor
Workstations, servers, and supercomputers
MIPS, by Silicon Graphics (ceased making MIPS-based systems in 2006).
SPARC, by Oracle (previously Sun Microsystems), and Fujitsu.
IBM's Power Architecture, used in many of IBM's supercomputers, midrange servers and workstations.
Hewlett-Packard's PA-RISC, also known as HP-PA (discontinued at the end of 2008).
Alpha, used in single-board computers, workstations, servers and supercomputers from Digital Equipment Corporation, Compaq and HP (discontinued as of 2007).
RISC-V, the open source fifth Berkeley RISC ISA, with 64 or 128-bit address spaces, and the integer core extended with floating point, atomics and vector processing, and designed to be extended with instructions for networking, IO, data processing etc. A 64-bit superscalar design, "Rocket", is available for download.
RISC processors are also used in supercomputers such as the K computer, the fastest on the TOP500 list in 2011, second at the 2012 list, and fourth at the 2013 list, and Sequoia, the fastest in 2012 and third in the 2013 list.

## Slide 26: CISC-based Processor
PDP-11, VAX, Motorola 68k, intel’s x86

## Slide 27
CISC
Emphasis on hardware
Includes multi-clock complex instructions
Memory-to-memory: "LOAD" and "STORE“ incorporated in instructions
Small code sizes, high cycles per second
Transistors used for storing complex instructions
RISC
Emphasis on software
Single-clock, reduced instruction only
Register to register: "LOAD" and "STORE“ are independent instructions
Low cycles per second, large code sizes
Spends more transistors on memory registers

## Slide 28: Complex Instruction Set Computer (CISC) processors, like the x86, have a rich instruction set capable of doing complex things with a single instruction. Such processors often have significant amounts of internal logic that decode machine instructions to sequences of internal operations (microcode).RISC architectures, in contrast, have a smaller number of more general purpose instructions, that might be executed with significantly fewer transistors, making the silicon cheaper and more power efficient. Like other RISC architectures, ARM cores have a large number of general-purpose registers and many instructions execute in a single cycle. It has simple addressing modes, where all load/store addresses can be determined from register contents and instruction fields.

## Slide 29: CISC Instruction Sets
  Complex Instruction Set Computer
  IA32 is example
Stack-oriented instruction set
  Use stack to pass arguments, save program counter
  Explicit push and pop instructions
Arithmetic instructions can access memory
  addq %rax, 12(%rbx,%rcx,8)
    requires memory read and write
    Complex address calculation
Condition codes
  Set as side effect of arithmetic and logical instructions
Philosophy
  Add instructions to perform “typical” programming tasks

## Slide 30: RISC Instruction Sets
  Reduced Instruction Set Computer
  Internal project at IBM, later popularized by Hennessy (Stanford) and Patterson (Berkeley)
Fewer, simpler instructions
  Might take more to get given task done
  Can execute them with small and fast hardware
Register-oriented instruction set
  Many more (typically 32) registers
  Use for arguments, return pointer, temporaries
Only load and store instructions can access memory
  Similar to Y86-64 mrmovq and rmmovq
No Condition codes
  Test instructions return 0/1 in register

## Slide 31: Further Reading
https://cs.stanford.edu/people/eroberts/courses/soco/projects/risc/risccisc/

## Slide 32
Hardware or Software component
Algorithm
Programming Language
Compiler
Instruction Set Architecture
Affects what?
Instruction count, CPI
Instruction Count, CPI
Instruction Count, CPI
Instruction Count, Clock Rate, CPI